BCC_SDR Design
Eric Brombaugh KC7GXA
Tom King KA6SOX

Design Goals

1) Direct Conversion LF, MF, HF multi-mode SDR Modem. (150khz-30mhz)

2) VHF and UHF Single Conversion SDR Modem. (50mhz-450mhz)

3) Internet Connected SDR receiver(Transmitter)

4) Ham Bands focus (160m-70cm)

5) Open Source Hardware

6) Low Cost

7) 0.2uV RX, +10dbm TX

8) Simplex, Half-Duplex or Full Duplex (including split band for Satellite work)

HARDWARE

Block Diagramme

Digital Section

Analogue Section

Receiver

Switch/RX SMA

Preamp

HF path: bypass switches, to 9865 rx transformer

VHF/UHF path: Switch, RX Mixer, IF Amp, Switch to 9865 rx transformer.

Transmitter

HF Path: 9865 TX transformer bypass swtiches to TX Amp, TX/RX switch TX(rx) SMA

VHF/UHF path: 9865 TX transformer, switch to TX mixer, Post amp with HPF, switch to TX Amp, TX/RX switch, TX(rx) SMA

Local Oscillators

Only used for VHF/UHF, 35-500mhz Single for Simplex only operation, 2 for Duplex/Split Band operation.

SOFTWARE

Control

FPGA

Data/Audio

REFERENCE DOCUMENTS