BCC_SDR Design
Eric Brombaugh KC7GXA
Tom King KA6SOX

Design Goals

1) Direct Conversion LF, MF, HF multi-mode SDR Modem. (150khz-30mhz)

2) VHF and UHF Single Conversion SDR Modem. (50mhz-450mhz)

3) Internet Connected SDR receiver(Transmitter)

4) Ham Bands focus (160m-70cm)

5) Open Source Hardware

6) Low Cost

7) 0.2uV RX, +10dbm TX

8) Simplex, Half-Duplex or Full Duplex (including split band for Satellite work)

HARDWARE

Block Diagramme

Digital Section

The BCC SDR system interfaces to the Blank Canvas Cape Spartan 6 (BCC S6) via a 40-pin Hirose FX2 connector which carries the following signals:
Pin	Name	Function
1	GND
2	NC
3	JA4	T/R Switch
4	JA5	TX CLOCK (driven from AD9865)
5	JA6	PGA0
6	JA7	PGA2
7	JB4	PGA4
8	JB5	AD9865 SPI Chip Enable (active low)
9	JB6	SPI MISO
10	JB7	TX Enable
11	JC4	RX0
12	JC5	RX2
13	JC6	RX4
14	JC7	TX0
15	JD4	TX2
16	JD5	TX4
17	JD6	PLL Latch Enable 0 (TX & RX synth, or optional TX only)
18	JD7	CLKOUT2 (driven from AD9865)
19	+5V
20	GND
21	GND
22	NC
23	JA0	SPI Port Expander Chip Select (active low)
24	JA1	RX CLOCK (driven from AD9865)
25	JA2	Reset (active low)
26	JA3	PGA1
27	JB0	PGA3
28	JB1	PGA5
29	JB2	SPI Clock
30	JB3	SPI MOSI
31	JC0	RX Enable
32	JC1	RX1
33	JC2	RX3
34	JC3	RX5
35	JD0	TX1
36	JD1	TX3
37	JD2	TX5
38	JD3	PLL Latch Enable 1 (Optional separate RX synth)
39	+5V
40	GND

The FPGA interface consists of the high-speed parallel connection to the AD9865 ADC / DAC, a SPI port with four possible targets (the AD9865, an 8-bit SPI port expander and two PLL synthesizers). The SPI port expander generates low-speed configuration signals for the AD9865 and the HF / VHF switch controls,

Bit	Function
0	Receive path HF / VHF switch output
1	Transmit path HF / VHF switch output
2	PLL 0 Lock detect input
3	PLL 1 Lock detect input
4	PLL 1 & 0 Chip Enable
5	AD9865 Mode control output
6	AD9865 Config control output
7	AD9865 Power Down output

Analogue Section

Receiver

Switch/RX SMA

Preamp

HF path: bypass switches, to 9865 rx transformer

VHF/UHF path: Switch, RX Mixer, IF Amp, Switch to 9865 rx transformer.

Transmitter

HF Path: 9865 TX transformer bypass swtiches to TX Amp, TX/RX switch TX(rx) SMA

VHF/UHF path: 9865 TX transformer, switch to TX mixer, Post amp with HPF, switch to TX Amp, TX/RX switch, TX(rx) SMA

Local Oscillators

Only used for VHF/UHF, 35-500mhz Single for Simplex only operation, 2 for Duplex/Split Band operation.

SOFTWARE

Control

FPGA

Data/Audio

REFERENCE DOCUMENTS